## Slide 1
Effect of Atmospheric SOx on Aminosilica Adsorbents for Air Capture
Steph Didas
EAS 6410
April 26, 2012

## Slide 2: Air Capture Technologies & CO2 Adsorption Mechanism
Solid Adsorbents
Caplow, J. Am. Chem. Soc., 1968.
Donaldson & Nguyen, Ind. Eng. Chem. Fundam., 1980.
CO2 rich air
CO2 lean air
amine-oxide
CO2-amine-oxide
Sorbent regen &
CO2 recovery
CO2 removal from air
CO2
Regeneration

## Slide 3: Supported Amine Adsorbents
Class 1: Physical impregnation
Class 2: Covalent tethering
Class 3: In situ polymerization
Li et al., ChemSusChem, 2010.
Bollini et al., J. Mater. Chem., 2011.
Class 1:
High amine content
Not stable
Class 2:
Low amine content
Stable
Class 3:
High amine content
Stable

## Slide 4: Sorbent Degradation from SOx in Flue Gas Streams
Khatri et al., Energy Fuels, 2006.
DRIFTS absorbance spectra during SO2 adsorption
DRIFTS absorbance spectra during SO2 temperature programmed desorption
SO2 irreversibly adsorbs forming heat stable corrosive salts
Flue gas SO2 concentrations 500-2000 ppm  What happens at air capture concentrations?

## Slide 5: Objective of Study
Estimate adsorbent deactivation due to SOx concentrations in the atmosphere based on reported data for flue gas degradation
6

## Slide 6: Adsorption Mechanism & Proposed Model
Belmabkhout & Sayari, Energy Fuels, 2010.
Diaf et al., J. Appl. Polym. Sci., 1994.
RNH2 + SO2
RNH2+ + SO2-
K
Assumptions:
[SO2] is equal to feed concentration due to constant supply
[RNH2+] = [SO2-] due to 1:1 stoichiometric ratio

## Slide 7: [SO2] Trends: Atlanta
Upper limit: 45 ppb
Lower limit: 5 ppb

## Slide 8: [SO2] Trends: Pittsburgh
Upper limit: 250 ppb
Lower limit: 5 ppb

## Slide 9: Atmospheric SO2 Adsorption Results
 | % of FG Upper Limit | % of FG Lower Limit
Atlanta | 0.47 | 0.95
Pittsburgh | 1.1 | 2.2
SO2 adsorption/degradation potential very low at harshest atmospheric conditions
Can set up capture stations at locations with less extreme variation

## Slide 10: Summary & Future Work
Atmospheric SOx degradation location dependent
  Should set up air capture station in low pollution area
  NOx degradation studies needed
    Flue gas streams 2500-1500 ppm vs. atmospheric levels of 80-5 ppb
    More complicated mechanism  data needed for additional products

## Slide 11: Questions?