## Slide 1: Coal Refuse FirE and pollution emissions
nicole swartwood
atmospheric chemistry
april 19, 2016

## Slide 2: Motivation
“The contribution of coal fires to the global pool of atmospheric CO2 is little known but potentially significant.” –USGS, 2009
Coal fire remediation project costs exceeds $1 million
  90% of these funds in PA and WV
  No accurate inventory unofficial estimates ~150 uncontrolled surface and underground mine fires in US as of 2003.

## Slide 3: What is coal refuse? aka Gob piles, slate dumps, coal refuge, and waste piles
EPA: waste products of coal mining, physical coal cleaning, and coal preparation operations containing coal, matrix material, clay and other organic and in organic material.
PA regulations: “any waste coal, rock, shale, slurry, culm, gob, boney, slate, clay and related materials, associated with or near a coal seam, which are either brought aboveground or otherwise removed from a coal mine in the process of mining coal or which are separated from coal during the cleaning or preparation operations. The term includes underground development wastes, coal processing wastes, excess spoil, but does not mean overburden from surface mining activities.”

## Slide 4: Chemical composition
Carbon makes up about 1/3 of
coal refuse.
Stewart, 1992.

## Slide 5: Coal refuse fires
Natural and anthropogenic
Difficult to extinguish
long lifetimes
Particularly dangerous if they reach original coal seam

## Slide 6: Mechanism
Notes: Particle size—smaller size exposese greater total surface area to oxidation, more rapid oxidation, but fine, tight packed can reduce air flow and reduce oxidation.

## Slide 7: Products of combustion
Gases
  Hydrocarbons
  Hydrogen
  Carbon monoxide
  Complete combustion: CO2 and H2O
  Others
  Particulates
  Products of incomplete combustion: carbon suspended as smoke.
Notes: Dependent on
o2 concentration in the pile – particle size, type of surface, and windspeed.
type of coal
relative humidity
moisture content of coal
type of refuse
temperature

## Slide 8: Fell Township, PA
a case study

## Slide 9: FELL TOWNSHIP, PA
December –May 2014
Notes: Covers approximately 7 acres in simpson PA /FELL TOWNSHIP/LACKAWANNA COUNTY
LIKELY STARTED BY BURNING TRASH, TIRES

## Slide 10: “Our air sampling during the peak of the fire indicated that the public was not at risk of inhaling dangerous fumes.” Northeast Regional Office Director, Mike Bedrin
http://thetimes-tribune.com/news/dep-fell-twp-fire-extinguished-1.1690008

## Slide 11
EPA
AirData

## Slide 12
Chart: 2012 [CO]
Chart: 2013 [CO]
Chart: 2014 [CO]
Chart: 2015 [CO]
Notes: National standard of 9 ppm for 8 hours

## Slide 13
Estimated .237 ppm increase in daily high average.

## Slide 14
Chart: 2012 [PM 2.5]
Chart: 2013 [PM 2.5]
Chart: 2014 [PM 2.5]
Chart: 
Notes: National standard of 12

## Slide 15
Estimated 4.38 ug/m3 increase in daily high average.

## Slide 16
Chart: 2013 [NO2]
Chart: 2014 [NO2]
Chart: 2012 [NO2]
Chart: 2015 [NO2]
Notes: 53 ppb over one year

## Slide 17
Estimated increase of 7.425 ppb, daily high average.

## Slide 18
Chart: 2012 [O3]
Chart: 2013 [O3]
Chart: 2014 [O3]
Chart: 2015 [O3]
Notes: 8 hours of 0.070

## Slide 19
Estimated 0.0006 ppm increase daily high average.

## Slide 20: Impacts
Health effects are unclear
  Research focuses on industrial combustion by products
  Chemical differences between industrial useful coal and coal refuse makes these studies weak.
Finkelman, 2004.

## Slide 21: references
EPA. 1978. Source Assessment: Coal Refuse Piles, Abandoned Mines and Outcrops, State of the Art.
Finkelman, R.B., 2004, Potential health impacts of burning coal beds and waste banks: International Journal of Coal Geology, v. 59, p. 19–24.
Stewart, B.R. and W.L. Daniels. 1992. Physical and Chemical Properties of Coal Refuse from Southwest Virginia: J. Environ. Qual, v. 21, p. 635-642.
USGS. 2009. Emissions from Coal Fires and Their Impact on the Environment: Fact Sheet.