## Slide 1: Evaluation of a potential HONO source: A case study in China
Kezhen Chong
April 21, 2020
EAS 6410 Term Project

## Slide 2: Outline
Introduction
Data and Methods
Results
Summary

## Slide 3: Nitrous acid (HONO)
Introduction | Data and methods | Results | Summary
Important OH source (Kleffmann, 2007 )
Source:
  OH + NO
  …
  heterogeneous reactions
    Aerosol surface
    Ground surface
HONO
NO
VOCs
OH

## Slide 4: Data and method
Introduction | Data and methods | Results | Summary
1-D Reginal chEmical trAnsport Model (REAM 1-D)
  30 layers in troposphere
  Concentrations of NO, , , CO and NMVOCs are constrained at 1 min time step
Ozone Photochemistry and Export from China Experiment (OPECE)
  March and April 2018
  Rural coastal site in a wetland reserve
  in Dongying, Shandong, China
  and aerosol surface area
  LOPAP (Long path absorption photometer) measured HONO surface concentration

## Slide 5: Observations and base simulation (OH + NO)
Introduction | Data and methods | Results | Summary
Heterogeneous reaction of
  On aerosol surface
  On ground surface
OH + NO is not enough

## Slide 6: HONO source parameterizations (Liu et al., 2014)
Introduction | Data and methods | Results | Summary
Simplified

## Slide 7: HONO source parameterizations
Introduction | Data and methods | Results | Summary
Aerosol heterogeneous uptake of :
First-order rate constant Ka for aerosol uptake of is:
where
is molecular diffusion coefficient of ;
is total aerosol surface area;
is particle radius, 0.1 ;
is the mean molecular speed of in the air;
and is sticking coefficient (reactive uptake coefficient) for on aerosol surface, 1e-6 (Kleffmen et al., 1998).

## Slide 8: HONO source parameterizations
Introduction | Data and methods | Results | Summary
Ground heterogeneous uptake of :
Instantaneous release of HONO into the first model layer resulted from dry deposition of , first-order HONO release rate coefficient is:
where is dry deposition velocity for , output from 3-D REAM
and f is the yield of HONO from reaching the surface: 0.08 which is large enough to reproduce observed HONO at night in Beijing (Liu et al. 2014).
(Liu et al. 2014)

## Slide 9: Simulation scenarios
Introduction | Data and methods | Results | Summary
Scenarios | Configuration
S0 | NO + OH + M HONO + M
S1 | S0 + aerosol uptake of (constant )
S2 | S0 + ground uptake of (constant )
Scenarios | Configuration
S0 | 
S1 | 
S2 | 

## Slide 10: Simulation results
Introduction | Data and methods | Results | Summary
Inaccurate constants taken from previous studies
Oversimplification of source parameterization
(Liu et al., 2014)

## Slide 11: f = 0.08 for ground source
Deposition velocity too small?
Scenarios | Configuration
S0 | NO + OH + M HONO + M
S1 | S0 + aerosol uptake of (constant )
S2 | S0 + ground uptake of (constant )
Scenarios | Configuration
S0 | 
S1 | 
S2 | 

## Slide 12: Future work
Introduction | Data and methods | Results | Summary
Photolytically enhanced ground source and aerosol source
Please see more details in the term paper
Scenarios | Configuration
S3 | S0 + photolytically enhanced aerosol uptake ()
S4 | S0 + photolytically enhanced ground uptake ()
Scenarios | Configuration
S3 | 
S4 | 

## Slide 13: Future work
Introduction | Data and methods | Results | Summary
Check deposition velocity first (to make sure it is correct)
Sensitivity tests to find the yield coefficient f for ground term to reproduce nighttime HONO -> f = 0.45 (more details in term paper)
Evaluate if f is reasonable
  If not reasonable, other HONO source needed
  if reasonable, check daytime production:
    If daytime is also reproduced, done
    If daytime still not enough:
      Photolytically enhanced ground source and aerosol source needed
Scenarios | Configuration
S3 | S0 + photolytically enhanced aerosol uptake ()
S4 | S0 + photolytically enhanced ground uptake ()
Scenarios | Configuration
S3 | 
S4 | 

## Slide 14: Thank you!